## Slide 1: Optimal Learning-Based Network Protocol Selection
Xiaoxi Zhang1, Siqi Chen2, Youngbin Im2,
Maria Gorlatoga3, Sangtae Ha2, Carlee Joe-Wong1
Workshop on ML for Systems @ISCA 2019

## Slide 2: Network needs are heterogeneous
Video Streaming
Augmented Reality
Internet of Things

## Slide 3: Today’s network management..
Relies on static pre-configurations
  E.g., pre-specifying routing algorithms used to determine flow paths
Or provides more flexible configurations but still requires manual intervention
  E.g., NFV and Radio access network Intelligence Controller

## Slide 4
An alternative solution: automated network management via learning the optimal policy/protocol configuration in real-time

## Slide 5: Why automated protocol selection
A pre-set policy/protocol can’t cover all possible scenarios
Existing policies/protocols can be utilized
Automated and dynamic approaches better adapt to changing environments

## Slide 6: Problem model
Flow 2
Network node
Flow 1
S1
S2
D1
D2
Flows arrive in a network online
  Each flow has a fixed size (the amount of data to transfer) and a pre-determined path
  Flows can share one or more links at any given time

## Slide 7: Problem model
Flow 2
Network node
Flow 1
S1
S2
D1
D2
Our decisions: choose one out of M pre-defined protocols to use on each link for each flow
  Protocols can be changed over time
TCP Reno
Wireless
link
UDP
TCP Cubic, TCP Vegas

## Slide 8: Problem model
Flow 2
Network node
Flow 1
S1
S2
D1
D2
TCP Reno
Wireless
link
UDP
TCP Cubic, TCP Vegas
Our goal: minimize the total flow completion time
  Completion time of a flow ≈ transmission delay on the bottleneck link

## Slide 9: Unknown information
Flow 2
Network node
Flow 1
S1
S2
D1
D2
TCP Reno
Wireless
link
UDP
TCP Cubic, TCP Vegas
Bandwidth capacity on each link at each time
Flow interactions under different protocols

## Slide 10: Stochastic flow interactions
For each flow i, on each link l, at each time t:
Transmission rate
Bandwidth
capacity
on each link l
at each time t
Total bandwidth utilization
Binary decision variable: protocol chosen for each flow
Bandwidth
partition weight

## Slide 11: Stochastic flow interactions
I.i.d. assumption on each parameter
Transmission rate
Bandwidth
capacity
on each link l
at each time t
Total bandwidth utilization
Binary decision variable: protocol chosen for each flow
Bandwidth
partition weight

## Slide 12: Multi-armed bandits (MAB)
Sequentially pull arms to maximize expected total reward
Arm 1
Arm 4
Arm 3
Arm 2
Bandit “arms” (unknown reward probabilities)

## Slide 13: Learning rate distributions
Transmission rate dependent with the protocol combination used for all co-existing flows
Problem: the number of possible protocol combinations exponential with the network size and number of co-existing flows
Protocol combination

## Slide 14: Sketch of our algorithm
On each link, at each time slot, independently do:
  Use the MAB-based algorithm to learn the dominant throughput (or weight for uniform total bandwidth utilization) of each pair of protocols, which is the transmission rate per flow achieved by flows using the better protocol in any protocol pair
  Select the protocol pair with the highest dominant throughput over all protocol pairs
  Select the better protocol from the chosen protocol pair for the flow with the shortest remaining size and the worse protocol in the chosen pair for other co-existing flows
  (This strategy shares the spirit with Shortest Remaining Time First)

## Slide 15: Theoretical guarantees
If the flows have the same bottleneck link and the total bandwidth utilization is uniform over all protocol combinations:
  Our strategy is optimal if the predictions of protocols are accurate
  The expected gap of the incurred completion time per flow between our algorithm and the optimum converges to zero

## Slide 16: Experiment set-up
Hop-by-hop transport layer protocol selection
Each node deployed on an Amazon EC2 instance, equipped with a TCP proxy; 50 Mbps capacity per link
Protocol choices: TCP CUBIC, Vegas, Reno, Westwood
50 Flows arriving in five batches spaced 3 seconds apart
Flow sizes uniformly drawn from [10, 20] Mb

## Slide 17: Performance comparison
Our algorithm OPSBC decreases the flow completion time by:
  66.18% compared with randomly selecting a protocol for each flow on each link (per-flow-random)
  43.27% compared with randomly selecting a protocol on each link for all flows to use (per-link-random)

## Slide 18: Thank you!
xiaoxiz2@andrew.cmu.edu
https://www.andrew.cmu.edu/user/xiaoxiz2/